## Slide 1: Takeaways from visit: Freiberg
Raka Adrianto
PhD student at IfU, Ecological System Design (ESD)
https://etn-sultan.eu/

## Slide 2: Take home learnings:
Geo statistical approach and spatial interpolation
Use: to capture heterogeneity in tailings body
Flowsheet techniques of chemical processes through chemical simulator or engineering-approach
Use: to complement upscaling studies

## Slide 3: Assessed systems: Two major routes
Sulfidic tailings
As secondary resources
Storage
Valorized products
Existing discharge
Status Quo
Resource recovery
Today’s focus
1
2
n

## Slide 4: Aim: parameterizing tailings storage
Why?
To update it with relevant parameters
Source: Kalgoorlie Tailings Facility, 2013
Tailings storage
facility
Un-boxing the “black” box
Input 1
Output 1
Output 2
… n
Input 2

## Slide 5: Workflow
Water quality prediction
Life cycle impact assessment
Data preparation
Geo statistics
1
2
3
Species emission into surroundings
Future tailings behavior (long term)
Details in the appendix

## Slide 6: Trial: hypothetical dataset (in S-GeMS)
x
y
z
0.5067
0.4222
0.3378
0.2533
0.1689
0.084
0
Experimental variogram
Estimation
Model : Spherical
Nugget : 0.0
Sill : 0.02
480
hard data

## Slide 7: Trial #2: hypothetical dataset (in Python)
Exploratory data analysis
3D Ordinary Kriging
Model : Spherical
Nugget : 0.0
Sill : 0.02
Executed with PyKrige library
Notes: https://pykrige.readthedocs.io/en/latest/index.html
B.S. Murphy, PyKrige: Development of a Kriging Toolkit for Python. AGU Fall Meeting, H51K-0753 (2014).
Dakota (Surfpack). C++ software with flexible interface that provides optimization algorithms, uncertainty quantification, parameter estimation, and sensitivity analysis for supporting computational models and simulators (Adams et al., 2009).
– PyKrige. Python package that performs 2-D and 3-D ordinary and universal kriging computation with flexible design for custom variogram implementation (Murphy, 2014).
– gstat. R package (computational core coded in C) that supports block kriging, simple, ordinary, and universal (co)kriging, and many other features (Pebesma, 2004), (Gräler et al., 2016). It is historically the leading software in this field

## Slide 8: Available tailings 2 (Plombières)
Data source: Van Campen, 2019

## Slide 9: Available tailings data 2 (Freiberg)
Chart: Minerals composition (%-w)
| Quartz | Muscovite | Pyrite | Chlorite | Biotite | Siderite | Ankerite | Orthoclase | Albite | Arsenopyrite | Calcite
 | 38.5 | 17.9 | 12 | 7.2 | 5.1 | 4.1 | 2.6 | 2.6 | 2.5 | 1.7 | 1.1

## Slide 10: Outlook
Simulate one condition (small sensitivities) – see own paper drawing

## Slide 11: Preliminary model and the expected outcome
Life cycle impact assessment
Chart: Time (year)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
pH | 8 | 8 | 7.8 | 7.8 | 7.7 | 7.6 | 2 | 2 | 2 | 2 | 2 | 2 | 1.8 | 1.6 | 1.6 | 1.6
SO4-- (aq) | 4.78e-06 | 5e-06 | 5.2e-06 | 2e-05 | 1.6e-05 | 1.2e-05 | 1e-05 | 9e-06 | 4.78e-06 | 4.4e-06 | 4.2e-06 | 3e-06 | 3e-06 | 3e-06 | 3e-06 | 3e-06
Inputs:
Tailings variables
Site-specific parameters
Realization #1
Model:
Water quality prediction
2
3
Cu
Impact:
Method: USETox (mid point)
Category: Freshwater ecotoxicity
Key: reactive transport PHREEQC model
Grid example
Geo statistics
Data preparation
1

## Slide 12: Next steps
LCA of Novel Processes Transition
Model integration:
parameterized tailings storage facility
Real samples collection to simulate full scale (uncertainties involved)
Full plan in appendix
Takeaways
Implementation
Notes: The question at the beginning remains unanswered: but we’re on our way, getting closer to it 

## Slide 13: Discussion with Markus + course (HSC Simulator)

## Slide 14: Outlook
Start with chemical engineering approach is expected
Draw lab-scale experiment and convert to plant-scale diagram (+ necessary unit operations)
Mass and energy balance – equipment estimation
Commercial chemical process simulator (costly)

## Slide 15: Thank you!  Particularly to ASB and D-BAUG community
: adrianto@ifu.baug.ethz.ch
5th D-BAUG Meet and Share Your Research
October 9, 2019

## Slide 16: Appendix
How is the overall workflow?
What is LCA by the way? How to quantify impacts?
Geochemical modelling with PHREEQC
Spatial interpolation of tailings variables (multivariate)
Hypothetical tailings body for model testing
Gantt chart of PhD project

## Slide 17: Workflow (data preparation and models)

## Slide 18: Definition and keywords
LCA
ISO 14040/44
Holistic
Transparency
“The compilation and evaluation of the inputs, outputs and potential environmental impacts of a product system throughout its life cycle”
Standardized

## Slide 19: Quantifying inputs and outputs – LCIA
Example of LCIA methods: IPCC, USETox, ReCiPe,… (Hauschild et al, 2013)
Global warming (kg CO2-eq)
…
1
25
298
-
…
Characterization factors (CFs)
324
Total
Climate change Eutrophication | Ecotoxicity Acidification
Other categories | 
Impact categories
Substance | Amount (kg)
… | …
Carbon dioxide (to air) | 1
Methane (to air) | 1
N2O (to air) | 1
Iron (from ground) | 1
… | …
Notes: Link to Paper:
Title: Identifying best existing practice for characterization modeling in life cycle impact assessment
https://link.springer.com/content/pdf/10.1007%2Fs11367-012-0489-5.pdf

## Slide 20: Reactive transport codes: PHREEQC
Simulation: Reactive Transport Modelling
Inputs for single realization
Minerals composition
Net precipitation
Transport parameters
Aqueous complexation reactions
Thermodynamics parameters (from database: Phreeqc)
Reference:
Phreeqc version 3 (Parkhurst, 2013)
Reactive transport codes for subsurface simulation (Steefel, 2014)
Infiltration
To bottom
Seepage 1
Seepage 2
Seepage n
Seepage 3

## Slide 21: Inputs for geochemical model
Mineral compositions and equilibrium constants
Kinetics and minerals surface
Geometry, flow, and transport parameters
Recharge water/ infiltration (precipitation – evaporation)
Biogeochemical reaction?
1
2
5
4
3

## Slide 22: Begin with synthetic spatial data
A. Complete data of synthetic tailings
Method: Numerical Stratigraphy
B. Take limited “samples” and populate grids with new (interpolated) values
Method: 2-point sampling prediction through variogram modelling + Kriging (modified ones)
More details, see “Interpolation/ geo statistics page”
Reference: Compositional Multipoint Geo statistics (Selia and Raimon, 2019)
Example: 1 feature (variable)

## Slide 23: Interpolation: Geo statistics prediction
Goal: Estimate the unknown values based on the known values proximities
Reference: Applied Spatial Data Analysis with R (Pebesma, 2013)
Variogram modelling
Pre-processing
Interpolation

## Slide 24: PhD Gantt chart: Raka
Tasks* | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 | 
 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2
Coursework + self-study, seminar… |  | O |  |  |  |  |  |  |  |  |  |  |  | 
Parameterized LCA of tailings storage facility |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Scientific paper 1a and 1b |  |  |  |  |  | O | O |  |  |  |  |  |  | 
LCA: Upscaling lab processes |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Scientific paper 2 |  |  |  |  |  |  |  |  |  | O |  |  |  | 
Multi-valorization pathways of case studies: complete assessment |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Scientific paper 3 |  |  |  |  |  |  |  |  |  |  |  | O | O | 
Thesis and defense |  |  |  |  |  |  |  |  |  |  |  |  |  | O
*a detailed Gantt chart is available